UDB4+ Parameter and waypoint storage in non volatile memory

Matthew Coleman – March 2012

Parameters are named pieces of data that are associated with the MAVlink communication protocol. Parameters are suitable for adjusting gains, calibrations and behaviour. MAVlink and protocols are described in these documents:

MAVlink Overview
Waypoint protocol
MAVlink Parameter Protocol

Once a parameter is adjusted, it may be desirable to store it in non volatile memory (does not forget when you switch the power off). UDB4 has an eeprom which is used for this. The following document describes how parameter storage is managed and how it can be used to change the behaviour of MatrixPilot.

## How to see and change parameters or waypoints

QGroundControl is the most capable parameter viewer at the time of writing. Using the parameter protocol it downloads the list of parameter names and the parameter values. It displays the parameters as a list which the user can edit and write back to the vehicle.

## How parameters are defined
MatrixPilot has a directory of parameters in parameters_table.c. For each entry in the parameter table, the following information is included:
- The character name of each parameter
- A reference to the RAM variable
- The size of the RAM variable (for data serialisation)
- If the variable is read only or read write.
- The data type of the internal variable
- The minimum allowed value of the parameter
- The maximum allowed value of the parameter

Each internal datatype has a read and write parser transfering information to/from the MAVlink datatypes. Some datatypes need scaling or range checking.

MAVlink supports transfer of most 8 to 32 bit datatypes. Only float and 32 bit int/uint is supported by qgroundcontrol at this time.

The min and max values are in the mavlink data type so they must be defined in the mavlink units.

This parameter table is too complex to build by hand, so it is built automatically from a database that is easier to write and maintain. This is called the parameter database.

## The datatypes table
Each parameter has a matrixpilot type defined. Each type has a load parser and a store parser. The enumeration names of the type and the parser function names are defined in the parameter database.

Note: The same parser can't be used for two different datatypes.
## The parameter database
The database is in XML format for easy man-machine readability. The database contains information about:
- How to build the parameters table
- How to build the data storage table
- How to build a table of datatypes

## Parameter table generator - pyparam
pyparam builds the following files from the database:
- parameter_table.c
  - List of parameters
  - List of extern memory locations
  - size of the parmaeter table
  - A list of matrixpilot datatype parsers
- parameter_datatypes.h
  - Enumeration of datatype parsers
  - Definition of each function of the datatype parsers
- nv_memory_table.c
  - List of data blocks
  - Count of the list of datablocks

parameter_table.h contains the type definitions used for the above tables.

Pyparam is found in the tools/pyparam directory. When pyparam runs, it automatically writes the new files into the MatrixPilot folder. You do not need to copy or move any files.

pyparam is written in python2.7. You must have python 2.7 installed on your machine if you wish to run pyparam. For more information on installation read here:
Python organisation homepage

## Editing the parameter database
The database has a schema associated with it. The schema describes how the information in the database should be formatted. A good editor will use the schema to help you make a database with the correct information. These are the best editors I have tried:

1. Eclipse
  1. Open source, free to use
  2. Multi platform
  3. Good graphical editor
  4. Works well as a python editor and debugger
  5. Needs python and/or xml modules adding (see section on Eclipse install)
2. Editix
  1. Windows only
  2. Free for non profit, non commercial use only
  3. Simple installation

## How data is managed
The storage manager is a light filesystem which allows blocks of data to be read and written. The files are not known as character names but have an enumeration instead. This enumeration is defined in matrixpilot.xml under the enumeration name MAV_NV_STORAGE_AREA.

These files/data areas can be individually created, written, read, cleared or deleted. The files have size and data validity checks.

## How parameters get into a data area (serialisation)

Each data area has a list of parameters that are associated with it. Items are read/written in order going through the list. In MatrixpPilot ram, variables will be scattered over the memory space. In non volatile memory, the variables are in order, one after the other (a data series).

The whole list of parameters is not written in one large lump. It is written in smaller blocks as defined by the database. The blocks are defined as datasets that you wish to behave in the same way.

Matrixpilot uses a lookup table (storage_table.c) to know which parameters to use in which block of data. Each entry in the storage table has the following information:
- Data storage area
- Index into the parameters for the first parameter of the block
- A count of parameters in the block
- Data storage flags
- Data storage callback

## Installing Eclipse

## When data is read or written
We wish to control which data blocks are read or written at a given moment of operation. Some data should be loaded at every startup. Some data should only be reloaded after an uncontrolled re-boot. This is controlled by the storage flags. These flags are defined in matrixpilot.xml by the enumeration MAV_NV_STORAGE_FLAGS.

- LOAD_ALL – Load everything regardless of flag
- SAVE_ALL – Save all regardless of flag
- LOAD_AT_STARTUP – Load at normal startup
- LOAD_AT_REBOOT – Load on reboot
- SAVE_AFTER_CAL – Save data after normal calibration cycle
- STORE_WAYPOINTS – Only when waypoints load/save is requested
- STORE_CALIB – Only when calibration data load/save is requested
- SAVE_MISSION – When mission load/Save is requested

The requried flags for each block of parameters are written into the parameter block of the parameter_database.xml. The database also defines an enumeration of the possible flags. This enumeration is written into parameter_datatypes.h when the files are generated by pyparam.

## What happens when data is reloaded
When some data is loaded from memory, MatrixPilot needs to change it's behaviour. For example, loading fixed radio trimpoints should stop the radio trim self calibration. The memory services communicates with matrixpilot using callbacks. The callback name is included in the parameter block of the database.

Note: The callbacks are only called when loading with startup or reboot flags set. They will not be called at any other time.

## Getting to data you can't see
Sometimes you wish to get to data that has no header defining it. An extern can be defined in the database. When the extern is defined in the database, use the type and name. Do not add the extern keyword.

## How to use QGroundControl with nv memory
QGroundControl has buttons in the engineering page for commanding data store/recall. We can add more control by doing the following:
1. Run QGC
2. Attach UDB
3. Add a new custom widget from the Tool Widgets->New Custom Widget menu.
4. In the new widget view, right click and choose import widget
5. Choose the file QGC Advanced memory storage widget.qgw from the tools/pyparam folder.

This will add a collection of buttons to the new widget view. These buttons add a selection of data saving, loading and clearing for different data areas.

If you need to add different button functions, read the MAV_CMD_PREFLIGHT_STORAGE_ADVANCED definition in matrixpilot.xml.

## General warnings
The non volatile memory services can't be used without mavlink.