I2C, EEPROM and storage on UDB4 with MatrixPilot

Matthew Coleman – Feb 2012

UDB4 has a microchip 24LC256 (32K*8) EEPROM onboard. This document describes the drivers for handling data between user and device.

## Background

To be compatible with the MatrixPilot system, any process that takes a significant length of time must be either low priority or be broken into small high priority parts. Reading or writing a serial connected non-volatile memory takes a significant amount of time. A 1kbyte write could take 100ms. Therefore the drivers are interrupt based with callbacks when the process has finished.

A callback will be running at high interrupt priority so it is important to keep processing to a minimum. If a longer process is needed, the callback must trigger a status or flag for the work to be done in a lower priority thread.

There are potential problems with maintaining flags over different interrupt priority levels. It is therefore important to restrict where the memory is accessed from. In this case, all service routines involving the memory are restricted to the low priority background process.

The memory services are split into four separate drivers:
1. I2C driver responsible for access to the I2C port. This driver knows nothing about the I2C device attached. It maintains access control between devices that wish to use I2C.
2. The non-volatile memory driver is responsible for doing device specific handling. In the case of 24LC256, it must break data writes into page sized chunks.
3. The storage driver is responsible for storing and recalling data in the correct memory location and checking it is correct.
4. The data services are responsible for serialising MatrixPilot data to/from storage. It knows all the data to be serialised, when the data is to be serialised and how to notify the MatrixPilot framework when serialisation is complete.

## I2C driver

This is generalised version of the magnetometer I2C driver written by Bill Premerlani. The main functionality is described in I2C.h.

There are three main functions for I2C access which are read, write and check acknowledge.

Read and write take the following parameters

unsigned char command	Single command byte specific to the device.
unsigned char* pcommandData,	Command data, usually the address.
unsigned char* prxData,PtxData, prxData	Data buffer from the user.
I2C_callbackFunc pCallback	Pointer to callback function from the user.
unsigned int rxSize, txSize	Written or read size

The write sequence is:
1. Start
2. Write command byte
3. Write command data
4. Write data buffer of size txSize
5. Stop
6. Trigger callback
The read sequence is:
1. Start
2. Write command byte
3. Write command data
4. Restart
5. Write command byte with read bit set
6. Read data of size rxSize
7. Stop
8. Trigger callback

The acknowledge is used to check if the device is present and is not busy writing data.
1. Start
2. Write command byte
3. Stop
4. Trigger callback

During all of these transactions, a busy flag is set to show that the I2C port can't be accessed by another device.

NOTE: At this time there is no device access timeout in the driver.

NOTE: The buffer passed as reference must exist in memory through the transaction. Local variables will disappear as the calling function exits.

## Non-volatile memory driver – 24LC256

Responsible for the control data required to drive a particular device. Controls access through read or write sequences.

The non volatile memory interface has two functions which are to read/write to/from a byte buffer. There functions take the following parameters.

unsigned char* rdBuffer, wrBuffer	Reference to caller owned buffer
unsigned int rdSize, wrSize	Number of bytes to read or write
NVMemory_callbackFunc pCallback	Reference to callback function

24CL256 requires 5ms approx to complete a write cycle. The I2C check acknowledge function is used to check that the write cycle has completed.

24LC256 has 64byte pages and write buffer. A write larger than 64bytes or crossing a page boundary must be split into chunks. The MCP24LC256_write_chunk functions checks how many bytes are left to write, limits to 64 and limits to the end of the page.

Limitation: The write cycle does not retry if it has a failure during write.

NOTE: The 24LC256 driver will not fully function without calling its service routine. Make sure this routine is called from the background thread only.

## Data Storage Driver

Responsible for organising how data is read/written to the nv memory. Maintains a table of data areas similar to a file allocation table. Filenames are not supported. The data areas are referred to by fixed data handles.

One of the major responsibilities is to prevent one data area overwriting or another.

Different data areas can have different data types which are handled and checked in different ways.
Self Managed: No checksum or header. The allocated space is the same as the requested area.
Checksummed structure: Adds a header to the data that contains pre-amble, data handle, version and checksum. These are all used to verify that the
Checksummed array: Manages an N sized array of M sized elements. Each element in the array has a checksum. This allows

Note: At this time, a self managed data area must be all at once. This can be changed to write a part.

Limitations:
The data storage driver is limited to a single nv_memory device. Data cannot be split between several storage locations.

## Data Services

Serialises data to/from the MatrixPilot variables. Uses user defined tables that define the data to be serialised and when to do it.

### Items list
A list of pointers to ram variables and the size of the variable in bytes. Data is serialised in list order. Note that a change in the list size results in a mismatch of data area size which resets all the data in that area.

### Service table
A list of items lists together with the information required to store them in the right way and at the right time. The table includes storage handle, data type, reference to an items list, the number of items in the list and the service/serialisation flags.

### Serialisation flags
These flags describe which items in the service table serialise when doing a load_all or store_all.

### Data Services Startup
On startup, data services will go through the service table checking if each entry in the table has a correct data area initialized by the data storage manager. If not, it will request that the data storage manager creates the data area. After checking/creating all the data areas, it will do data reload.

### Automatic data reload
Data services automatically does a data reload at startup. This happens as soon as the data manager It will set the LOAD_AT_STARTUP or LOAD_AT_REBOOT flags depending on hard or soft reboot. The lists that you wish to be reloaded at these times must have the appropriate flags set in the table.
If a data area fails to reload because it has not been initialised, data services will not attempt to serialise to working memory.

### Serialisation callbacks
There are two callbacks:
Pre serialisation callback (planned): Called before data has been committed to memory. This callback must return true/false to indicate if serialisation is to continue. Contains a boolean parameter indicating if data loading was a success.
Post serialisation callback: Called after automatic reload of data to memory during wither warm or hard reboot. This is not called when storing data to nv memory.

## NV Memory options
There is an options file that controls some behaviours of the library. The options are:
1. USE_NV_MEMORY: Used to switch on/off the compilation of the library into MatrixPilot.
2. MANUAL_ERASE_TABLE: Reformats/resets the data storage file allocation to erase all data. Note that this actions does not attempt to modify the data. I the same file location is chosen for a file then it will find a correct data at the location and attempt to use it. Using manual erase table is not a guarantee that you will have no data.

NV memory options also contain USE_FLEXIFUNCTION_MIXING. This is temporary.
## Driver and services implementation within MatrixPilot

The I2C driver and its callbacks run at high priority interrupt level. These processes must not consume much processor time. They must trigger a low priority process to service the longer processing needs. Each of the layers of the service must maintain its own state.

### Software interrupts using Events
This is a list of events that trigger running a callback at lowest interrupt priority. The events can be triggered from any interrupt priority. Triggering an event triggers the low priority interrupt. Since it is the lowest priority interrupt, triggering an event will not interrupt whatever is being done at that time. The triggering process will continue to complete.

The events and callbacks are not fixed at compile time. The table of events is built at runtime. A user of events must register its callback by calling register_event(pcallback). This returns an integer handle to the callback. Triggering an event is done using the trigger_event(handle) function.

The benefit of event registration is that events does not need to know anything about the users. It is therefore easy to maintain for different builds and is quite scalable.

WARNING: Events has a fixed amount of space available for event registration. In events.c the value MAX_EVENTS defines this. If this space is exceeded, register_event will return with value INVALID_HANDLE.

### Initialisation and triggering from background
Background was chosen as the most appropriate and clean place to put the event triggers as it runs at 40Hz. For this reason the initialisation was also placed in background. Once software timers are implemented, it may be appropriate to move initialisation from background and into libUDB.

### Isolation of services code
The USE_NV_MEMORY define is used wherever MatrixPilot includes the libraries or uses its functions to not include them in the compile. There are two main locations of use. This is in background.c and MAVlink.c. The USE_NV_MEMORY define also stops the service libraries included in the project from consuming the extra variables space used for buffers and states. Note that the I2C driver does do this.

## Planned work

### Remove I2C drivers from USE_NV_MEMORY selected services
This will be done so that other devices can use the I2C port.

### Event re-triggering
The software interrupts are only triggered by the background process. If you have a long task to do with many steps, it is dependent on the rate of the background process being able to pump the messages around. It is possible to trigger the events and its interrupt when necessary. This will accelerate the process.

### Software timers
There is a software timer library that can be used to trigger events. The software timers can be registered in the same way that the events are. Each software timer holds a value that is the trigger time. Whenever this completion time is exceeded, the event will trigger and the completion time incremented by the repeat period. Each timer has the option of running once or continuously.

The software timer is dependent on have a fast tick clock for good accuracy. This is not implemented within MatrixPilot. Software timers add a noticeable extra load to the processing. Therefore this implementation will wait until the system clock has been increased from the 8MHz to a higher value.

Software timers will remove the need for the manual triggering of the events within the background task. This will assist with maintainability as the background code does not need to change when adding or removing a new service.