I2C, EEPROM and storage on UDB4 with MatrixPilot

Matthew Coleman – Jan 2012

UDB4 has a microchip 24LC256 (32K*8) EEPROM onboard. This document describes the drivers for handling data between user and device.

## Background

To be compatible with the MatrixPilot system, any process that takes a significant length of time must be either low priority or be broken into small high priority parts. Reading or writing a serial connected non-volatile memory takes a significant amount of time. A 1kbyte write could take 100ms. Therefore the drivers are interrupt based with callbacks when the process has finished.

A callback will be running at high interrupt priority so it is important to keep processing to a minimum. If a longer process is needed, the callback must trigger a status or flag for the work to be done in a lower priority thread.

There are potential problems with maintaining flags over different interrupt priority levels. It is therefore important to restrict where the memory is accessed from. In this case, all service routines involving the memory are restricted to the low priority background process.

The memory services are split into three separate drivers:
1. I2C driver responsible for access to the I2C port. This driver knows nothing about the I2C device attached. It maintains access control between devices that wish to use I2C.
2. The non-volatile memory driver is responsible for doing device specific handling. In the case of 24LC256, it must break data writes into page sized chunks.
3. The storage driver is responsible for organising data and checking it is correct.

## I2C driver

This is generalised version of the magnetometer I2C driver written by Bill Premerlani. The main functionality is described in I2C.h.

There are three main functions for I2C access which are read, write and check acknowledge.

Read and write take the following parameters

unsigned char command	Single command byte specific to the device.
unsigned char* pcommandData,	Command data, usually the address.
unsigned char* prxData,PtxData, prxData	Data buffer from the user.
I2C_callbackFunc pCallback	Pointer to callback function from the user.
unsigned int rxSize, txSize	Written or read size

The write sequence is:
1. Start
2. Write command byte
3. Write command data
4. Write data buffer of size txSize
5. Stop
6. Trigger callback
The read sequence is:
1. Start
2. Write command byte
3. Write command data
4. Restart
5. Write command byte with read bit set
6. Read data of size rxSize
7. Stop
8. Trigger callback

The acknowledge is used to check if the device is present and is not busy writing data.
1. Start
2. Write command byte
3. Stop
4. Trigger callback

During all of these transactions, a busy flag is set to show that the I2C port can't be accessed by another device.

NOTE: At this time there is no device access timeout in the driver.

NOTE: The buffer passed as reference must exist in memory through the transaction. Local variables will disappear as the calling function exits.

## Non-volatile memory driver – 24LC256

Responsible for the control data required to drive a particular device. Controls access through read or write sequences.

The non volatile memory interface has two functions which are to read/write to/from a byte buffer. There functions take the following parameters.

unsigned char* rdBuffer, wrBuffer	Reference to caller owned buffer
unsigned int rdSize, wrSize	Number of bytes to read or write
NVMemory_callbackFunc pCallback	Reference to callback function

24CL256 requires 5ms approx to complete a write cycle. The I2C check acknowledge function is used to check that the write cycle has completed.

24LC256 has 64byte pages and write buffer. A write larger than 64bytes or crossing a page boundary must be split into chunks. The MCP24LC256_write_chunk functions checks how many bytes are left to write, limits to 64 and limits to the end of the page.

Limitation: The write cycle does not retry if it has a failure during write.

NOTE: The 24LC256 driver will not fully function without calling its service routine. Make sure this routine is called from the background thread only.

## Data Storage Driver

Responsible for organising how data is read/written to the nv memory. Maintains a table of data areas similar to a file allocation table. Filenames are not supported.

One of the major responsibilities is to prevent one data area overwriting or another.

Different data areas can have different data types which are handled and checked in different ways. A checksum can be applied to the whole data area or to individual array elements within the area. Alternatively the data area can be maintained entirely by the user.

Limitations:
The data storage driver is limited to a single nv_memory device. Data cannot be split between several storage locations.